## Slide 1: Qualcomm FSM10055 LSDK Build on LX2160ARDB
Keifer Lee
V1.3
2021/5/25

## Slide 2: Download code from ZC12 Git server
wget http://10.113.8.169/repo && chmod +x repo && sudo cp repo /usr/local/bin/
repo init -u git://10.113.8.169/hinoki/manifests -b qcom_release_pcieslot2
  輸入user name/email
  輸入Bugzilla Project/ID/PWD
repo sync -j4

## Slide 3: Build environment setup
Build NXP LSDK
  Ubuntu 18.04
  執行flex-builder 時自動會裝apt 套件, 須先把sudo設成不需密碼
    可參考：https://www.mxp.tw/291/
內網需先設定proxy (2F Lab 環境不需要設定):
  /etc/apt/apt.conf (若不存在則自行建立)
    Acquire::http::Proxy "http://[ID]:[PWD]@10.113.1.14:3128";
    Acquire::https::Proxy "http://[ID]:[PWD]@10.113.1.14:3128";
  ~/.bashrc
    export http_proxy=http://[ID]:[PWD]@10.113.1.14:3128
    export https_proxy=http://[ID]:[PWD]@10.113.1.14:3128

## Slide 4: NXP Layerscape Software Development Kit (LSDK)
LSDK is a complete Linux kit for NXP QorIQ Arm-based SoC’s
It is a hybrid form of a Linux distribution because it combines the following major components to form a complete Linux system.
• NXP firmware components including:
— Trusted Firmware-A (TF-A), a reference implementation of secure world software for
Armv7-A and Armv8-A.
— NXP peripheral firmware components for DPAA1, DPAA2, and PPFE.
• NXP boot loaders. Two are offered:
— U-Boot, based on denx.de plus patches.
— UEFI, based on TianoCore.
• NXP Linux kernel, based on kernel.org upstream plus patches.
• NXP added user space components.
• Ubuntu standard user space file set (user land), including compilers and cross compiler.

## Slide 5: Build LSDK
參考NXP Layerscape SDK user guide (LSDKUG_Rev20.04_290520.pdf)
cd <ZC27_root>/flexbuild-lsdk2004
. ./setup.env
./build_lsdk.sh
  自動下載src/bin (參考configs/build_lsdk.cfg)
  自動安裝apt/pip 套件
  自動build (預設只build bootpartition 和firmware，但rfs是prebuilt)
  自動產生image

## Slide 6: Build LSDK @ 2F Lab VM
Ubuntu 18.04 server (可build flexbuild)
IP: 192.168.41.18
account/password: compal/compal
Build LSDK :
  cd flexbuild_lsdk2004
  . ./setup_2f.env
  ./build_lsdk_2f.sh

## Slide 7: flex-builder command options
cd flexbuild_lsdk2004
. ./setup.env
全build (sdboot):
  flex-builder -m lx2160ardb_rev2 –i auto
只build rfs partition (Ubuntu userland):
  flex-builder -m lx2160ardb_rev2 -i mkrfs
  flex-builder -m lx2160ardb_rev2 -c apps
  flex-builder -m lx2160ardb_rev2 -i merge-component
  flex-builder -m lx2160ardb_rev2 -i packrfs
只build fw (sdboot):
  flex-builder -m lx2160ardb_rev2 -b sd -i mkfw
只build linux:
  flex-builder -m lx2160ardb_rev2 -c linux
只build boot partition (含Build linux, boot script, initrd等等…):
  flex-builder -m lx2160ardb_rev2 -i mkbootpartition
第一次執行會先去裝apt 套件

## Slide 8: LSDK output under $FBDIR/build/images/
bootpartition_LS_arm64_lts_4.19_[timestamp].tgz
  The boot partition includes kernel image, DTB, distro boot script, secure boot headers, tiny initrd etc.
  Mounted at /boot
firmware_lx2160ardb_rev2_uboot_sdboot.img
firmware_lx2160ardb_rev2_uboot_emmcboot.img
firmware_lx2160ardb_rev2_uboot_xspiboot.img
  LSDK composite firmware consists of RCW/PBL, ATF, Bootloader(U-Boot or UEFI), secure headers, Ethernet MAC/PHY firmware
rootfs_lsdk2004_ubuntu_main_arm64_[timestamp].tgz
  FETCH_PREBUILT_LSDK_RFS=n
rootfs_lsdk2004_yocto_tiny_arm64.cpio.gz
  Yocto Linux
flex-installer
  NXP提供的install script

## Slide 9: Flash LSDK to SD card (from X86 PC)
flex-installer (under build/images/)
  SD card 需16G以上, SD size決定下面的partition 大小
  sudo ./flex-installer -i pf -p 4P=1G:2G:6G:6G -d [device]
  sudo ./flex-installer -b [bootpartition] -r [rootfs] -R [rootfs_backup] -f [firmware] -d [device]
  X86 上接讀卡機的SD card dev 類似 /dev/sde
Umount SD card
  sudo umount /mnt/sde1
  sudo umount /mnt/sde2
  sudo umount /mnt/sde3
  sudo umount /mnt/sde4

## Slide 10: Flash LSDK to eMMC (from SD card)
把image放在SD 的rootfs 裡
  /root/bootpartition_LS_arm64_lts_4.19.tgz
  /root/firmware_lx2160ardb_rev2_uboot_emmcboot.img
  /root/rootfs_lsdk2004_ubuntu_main_arm64.tgz
插入SD, 開機到 kernel
flex-installer (內建指令)
  flex-installer -i pf -p 4P=1G:2G:57G:57G -d /dev/mmcblk1
  flex-installer -b [bootpartition] -r [rootfs] -f [firmware] -d /dev/mmcblk1
  PS. Emmc dev node固定為 /dev/mmcblk1
強制用eMMC的uboot+kernel開機
  DIP switch SW1[0:3] 切成 1001
  移除SD card
  開機

## Slide 11: Flash LSDK to eMMC (from tftp server)
插入SD, 開機到 kernel
網路線接上DPMAC.3 (靠近光纖孔的10G RJ45)
  ifconfig eth1 10.113.31.30 netmask 255.255.255.0 up
用tftp 從X86 tftp server 一個一個抓下來 (-g: get, -r: remote) (約3MB/s)
  tftp -gr bootpartition_LS_arm64_lts_4.19.tgz 10.113.31.20
  tftp -gr firmware_lx2160ardb_rev2_uboot_emmcboot.img 10.113.31.20
  tftp -gr rootfs_lsdk2004_ubuntu_main_arm64.tgz 10.113.31.20
flex-installer (內建指令)
  flex-installer -i pf -p 4P=1G:2G:57G:57G -d /dev/mmcblk1
  flex-installer -b [bootpartition] -r [rootfs] -f [firmware] -d /dev/mmcblk1
  PS. Emmc dev node固定為 /dev/mmcblk1
強制用eMMC的uboot+kernel開機
  DIP switch SW1[0:3] 切成 1001
  移除SD card
  開機

## Slide 12: Flash LSDK to eMMC (from tftp server)
補充：在X86 Ubuntu 16.04/18.04 架 tftp server
  sudo apt install -y tftpd-hpa tftp-hpa
tftp server 預設路徑是/var/lib/tftpboot/
tftp server config：/etc/default/tftpd-hpa

## Slide 13: Flash LSDK to 64MB NOR flash dev#0 (from SD or eMMC)
只需燒firmware_xxx_uboot_xspiboot.img, 即包含firmware+boot+rfs
把image放在SD 或emmc 的rootfs 裡
  SD: mmc 0:4
  eMMC: mmc 1:4
u-boot 指令 (用SD或eMMC開機)
  以image 放在SD 卡的 /root/ 下為例, 若eMMC 則改為 mmc 1:4
  > load mmc 0:4 $load_addr /root/firmware_lx2160ardb_rev2_uboot_xspiboot.img
  > sf probe 0:0
  > sf erase 0 +$filesize && sf write $load_addr 0 $filesize
強制用NOR flash 的uboot+kernel開機
  DIP switch SW1[0:3] 切成 1111開機, u-boot 指令：
  > setenv boot_target
  > boot

## Slide 14: Tip: Replace current boot partition when emmcboot or sdboot
Copy bootpartition_XXX.tgz from X86 PC to OAK
  cd flexbuild_lsdk2004/build/images/
  scp bootpartition_XXX.tgz user@<OAK_IP>:~/
SSH login to OAK and unzip
  ssh user@<OAK_IP>
  sudo tar xfmv bootpartition_XXX.tgz -C /boot/
Reboot
  reboot

## Slide 15: Tip: Replace emmc boot partition when sdboot
Copy bootpartition_XXX.tgz from X86 PC to OAK
  cd flexbuild_lsdk2004/build/images/
  Scp bootpartition_XXX.tgz user@<OAK_IP>:~/
SSH login to OAK and unzip
  ssh user@<OAK_IP>
  sudo mkdir -p /mnt/rfs
  sudo mount /dev/mmcblk1p4 /mnt/rfs
  sudo tar xfmv /home/user/bootpartition_XXX.tgz -C /mnt/rfs/
Reboot
  reboot

## Slide 16: Boot LX2160ARDB
Connect PC to UART1
  sudo minicom -s -w
Default LSDK account(id/pwd):
  root/root  不支援ssh登入
  user/user
Set time
  timedatectl set-ntp 0
  timedatectl set-timezone “Asia-Taipei”
  timedatectl set-time “2020-09-07 02:44:55”
Set NIC (NXP預設是1G MAC17[eth1] and 40G MAC2[eth0])
  ls-addni dpmac.3  建立dpmac.3 (10Gb) 的dpni
  ls-addni dpmac.4  建立dpmac.4 (10Gb) 的dpni
  ls-addni dpmac.18  建立dpmac.18 (1Gb) 的dpni
  dhclient